## Slide 1
CASE STUDY
Performance Evaluation of Hybrid Automatic Repeat Request (HARQ) Schemes in 5G NR under Fading Channels
Team Members:
K.AZAAN AHAMED - 23BEC0362
S.S.SREENITHIE- 23BEC0423
ADARSH- 23BML0100
WIRELESS AND MOBILE COMMUNICATIONS - BECE317L

## Slide 2
1
Introduction
5G Communication Challenges
Fifth-generation (5G) wireless networks demand ultra-high reliability and ultra-low latency to support critical applications including autonomous vehicles, industrial automation, and remote surgery.
High Reliability: 99.999% packet delivery requirement
Low Latency: < 1ms end-to-end delay target
Wireless Channel Impairments
Noise
Thermal & interference
Interference
Co-channel & adjacent
Fading
Multipath & shadowing
Impact on Communication Quality
These impairments cause packet errors and packet loss, directly degrading the Quality of Service (QoS) and user experience.
→
Errors → Packet Loss
→
Packet Loss → Reduced QoS
HARQ: The Solution
Hybrid Automatic Repeat Request (HARQ) combines Forward Error Correction (FEC) with Automatic Repeat Request (ARQ) to significantly improve link performance.
FEC
Error Correction
+
ARQ
Retransmission
=
HARQ
Enhanced Reliability

## Slide 3
2
SDG Goals Alignment
HARQ technology directly contributes to the United Nations Sustainable Development Goals (SDGs), enabling sustainable and inclusive communication infrastructure worldwide.
9
SDG 9
Industry, Innovation & Infrastructure
Reliable Communication Systems: HARQ ensures robust data transmission for industrial IoT and smart manufacturing
Infrastructure Resilience: Enables critical infrastructure monitoring and control systems
Technological Innovation: Drives advancement in wireless communication standards
11
SDG 11
Sustainable Cities & Communities
Smart Connectivity: Powers IoT networks for smart city applications
Intelligent Transport: Supports autonomous vehicles and traffic management systems
Public Safety: Enables reliable emergency communication networks
4
SDG 4
Quality Education
Advanced Learning: Facilitates remote education and virtual classrooms
Research Collaboration: Enables seamless international academic cooperation
Digital Inclusion: Provides reliable connectivity for underserved regions
Spectrum Efficiency Impact
HARQ enables efficient spectrum usage, maximizing data throughput while minimizing interference—critical for sustainable wireless communication growth.

## Slide 4
3
Problem Statement
Key Challenges in 5G Communication
1
High Error Rates in Fading Channels
Wireless fading channels cause significant signal degradation, leading to high Bit Error Rates (BER) that compromise data integrity.
2
Increased Delay from Retransmissions
Multiple retransmissions introduce latency, violating 5G's ultra-low latency requirements for time-sensitive applications.
3
Trade-off: Reliability vs Throughput
Achieving high reliability often requires sacrificing throughput, creating a fundamental optimization challenge.
Limitations of Conventional ARQ
Traditional Automatic Repeat Request (ARQ) schemes are inefficient in poor channel conditions, discarding valuable received information and retransmitting entire packets repeatedly.
Conventional ARQ Efficiency
LOW
Poor performance in fading environments
Research Gap
There is a critical need for optimized HARQ schemes specifically designed for 5G requirements that can:
Maximize throughput while maintaining reliability
Minimize retransmission delays
Adapt to varying channel conditions
Efficiently utilize spectrum resources

## Slide 5
4
Research Objectives
Primary Objective
To comprehensively analyze and compare the performance of three major HARQ schemes in 5G New Radio (NR) under realistic fading channel conditions.
Scheme Analysis
1
Type I HARQ
Basic retransmission without combining
2
Chase Combining (CC)
Signal-level combining approach
3
Incremental Redundancy (IR)
Code-level combining approach
Performance Metrics
Bit Error Rate (BER)
Measure of data integrity and reliability
Lower is better
Throughput
Data rate efficiency and spectrum utilization
Higher is better
Channel Conditions
Study behavior under Rayleigh and Rician fading channels to evaluate real-world performance across diverse wireless environments.

## Slide 6
5
System Architecture
Figure 1: Complete transmission system model for HARQ performance evaluation in 5G NR.
Data
Generation
→
Channel
Encoding
→
Modulation
(QAM)
→
Fading
Channel
Rayleigh / Rician
↓
HARQ
Process
Type I / CC / IR
→
Decoder
(FEC)
→
Performance
Metrics
BER / Throughput
Fading Models
Rayleigh: No line-of-sight
Rician: With line-of-sight
HARQ Mechanisms
Type I: Simple ARQ
CC: Signal combining
IR: Code combining
Measurements
BER: Error probability
Throughput: Data rate

## Slide 7
6
Methodology Overview
A comprehensive MATLAB-based simulation framework was developed to evaluate HARQ performance under controlled channel conditions.
Simulation Components
1
Transmission System Model
Complete end-to-end communication chain
2
Fading Channel Models
Rayleigh and Rician distributions
3
HARQ Implementations
Type I, CC, and IR schemes
Performance Evaluation
BER vs SNR Analysis
Measure bit error rate across different signal-to-noise ratios
Throughput Measurement
Calculate effective data rate under various conditions
Comparative Analysis
Direct comparison of all three HARQ schemes
Simulation Parameters
Channel coding: Turbo/LDPC | Modulation: 16-QAM, 64-QAM | SNR range: 0-20 dB | Maximum retransmissions: 4

## Slide 8
7
Approach 1: Type I HARQ
Mechanism Overview
Type I HARQ is the simplest form of hybrid ARQ, combining Forward Error Correction (FEC) with basic retransmission. It represents the baseline approach for error recovery in wireless communication.
Operational Flow
1
Transmit encoded data packet
2
Receiver performs error detection (CRC)
3
If error detected → send NACK
4
Discard previous packet
5
Retransmit same data
Key Characteristics
No Combining at Receiver
Previous transmissions are discarded—only the latest packet is used for decoding.
Independent Retransmissions
Each retransmission is treated as an independent event with no memory of past signals.
Simple Error Detection
Uses Cyclic Redundancy Check (CRC) for error detection before FEC decoding.
Conceptual Insight
Type I HARQ provides minimal complexity but sacrifices spectral efficiency by not utilizing information from previous failed transmissions.

## Slide 9
8
Type I HARQ: Analysis & Performance
Advantages
Low Complexity
Minimal computational requirements at both transmitter and receiver
Easy Implementation
Straightforward design with simple state machine
Low Memory Requirements
No need to store previous transmissions
Disadvantages
Poor Spectral Efficiency
Wasted bandwidth due to repeated full-packet retransmissions
Higher Retransmissions
More retransmissions needed in poor channel conditions
Lower Throughput
Reduced effective data rate, especially at low SNR
Performance Characteristics
Figure 2: Type I HARQ Performance
Simulated BER vs SNR for Type I HARQ in Rayleigh fading channel
Critical Assessment
High BER in fading conditions makes Type I HARQ unsuitable for 5G high data rate requirements.
BER at 10 dB SNR
~10⁻²
Throughput Efficiency
~60%

## Slide 10
Code Link: https://drive.google.com/file/d/1dda6jJY28kotadnWUhL9A8lzhUtEJBAd/view?usp=sharing

## Slide 11
9
SECTION 4.1
Approach 2: Chase Combining (CC)
Mechanism Overview
Chase Combining (CC) improves upon Type I HARQ by combining multiple received copies of the same packet, accumulating signal energy to enhance detection reliability.
Operational Flow
1
Transmit encoded data packet
2
If error → send NACK
3
Store previous signal in buffer
4
Retransmit same encoded packet
5
Combine all copies using MRC
Core Concept: Signal Energy Accumulation
Each retransmission adds coherent signal energy while noise adds incoherently, improving the effective SNR.
Equation 1: Combined SNR
SNRtotal = SNR₁ + SNR₂ + ... + SNRn
Maximum Ratio Combining (MRC): Optimal linear combining technique
Soft Combining: Operates at signal level before decoding
Same Redundancy: Identical parity bits in each retransmission
Conceptual Insight
CC provides diversity gain by exploiting multiple independent fading realizations, significantly improving reliability in time-varying channels.

## Slide 12
10
Chase Combining: Analysis & Performance
Advantages
Improved Reliability
Significantly better than Type I HARQ
Better SNR Performance
Effective SNR increases with each retransmission
Diversity Gain
Exploits time diversity in fading channels
Disadvantages
Increased Memory
Requires buffer storage for soft decisions
Moderate Complexity
MRC operations add computational overhead
Same Code Rate
No coding gain improvement
Performance Characteristics
Figure 3: Chase Combining Performance
Simulated BER vs SNR comparison: Type I vs Chase Combining
Performance Summary
BER at 10 dB SNR
~10⁻³
Throughput Efficiency
~75%
Reduced BER and moderate throughput improvement over Type I HARQ.

## Slide 13
Code Link : https://drive.google.com/file/d/1kU1ZefZHrEepkwp1Bvz3mE7fPYl0F24M/view?usp=sharing

## Slide 14
11
Approach 3: Incremental Redundancy (IR)
Mechanism Overview
Incremental Redundancy (IR) represents the most advanced HARQ scheme, transmitting different parity bits in each retransmission to gradually increase coding redundancy and improve error correction capability.
Operational Flow
1
Transmit initial coded packet
2
If error → send NACK
3
Store received packet
4
Retransmit different parity bits
5
Combine all transmissions for decoding
Core Concept: Gradual Redundancy Increase
Each retransmission adds new parity information, effectively lowering the code rate and increasing error correction capability.
1st Transmission:
Code Rate R = 1/2
2nd Transmission:
Code Rate R = 1/3
3rd Transmission:
Code Rate R = 1/4
Soft Combining: Operates at code level with advanced decoding
Coding Gain: Additional gain from code combining
Rate Compatibility: Uses rate-compatible punctured codes
Conceptual Insight
IR provides both diversity gain (like CC) and coding gain, achieving the best error performance among all HARQ schemes.

## Slide 15
12
Incremental Redundancy: Analysis & Performance
Advantages
Best Error Performance
Lowest BER among all HARQ schemes
High Throughput
Optimal spectrum utilization
Efficient Bandwidth Usage
Different parity bits maximize information
Coding + Diversity Gain
Both types of gain combined
Disadvantages
High Complexity
Advanced encoding/decoding required
Advanced Coding Required
Needs rate-compatible codes (Turbo/LDPC)
Higher Memory
Store multiple different transmissions
Performance Characteristics
Figure 4: Incremental Redundancy Performance
Simulated BER comparison: All three HARQ schemes
Performance Summary
BER at 10 dB SNR
~10⁻⁴
Throughput Efficiency
~85%
Lowest BER and best overall performance—ideal for 5G applications.

## Slide 16
Code Link: https://drive.google.com/file/d/1CXkximxC0kV0OQwOXhVA5ePVRsdiFDlN/view?usp=sharing

## Slide 17
13
Comparative Results & Discussion
BER Performance
Lower is Better
1. Incremental Redundancy
BEST
2. Chase Combining
GOOD
3. Type I HARQ
POOR
Throughput
Higher is Better
1. Incremental Redundancy
BEST
2. Chase Combining
GOOD
3. Type I HARQ
POOR
Retransmissions
Lower is Better
1. Type I HARQ
HIGHEST
2. Chase Combining
MODERATE
3. Incremental Redundancy
LOWEST
Figure 5: Comprehensive Performance Comparison
Key Observations
IR performs best under fading conditions with coding + diversity gain
CC provides balance between complexity and performance
Type I is least efficient but simplest to implement

## Slide 18
Code Link: https://drive.google.com/file/d/1zRtiz0Se1VHyuoPNnd8NCS2iN9XQrdyF/view?usp=sharing

## Slide 19
14
Applications of HARQ in 5G
HARQ schemes are fundamental to enabling diverse 5G use cases, from ultra-reliable low-latency communications to massive machine-type communications.
5G NR Systems
Core component of 5G New Radio (NR) physical layer, ensuring reliable data transmission across all deployment scenarios.
• Enhanced Mobile Broadband (eMBB)
• Ultra-Reliable Low Latency (URLLC)
• Massive Machine Type (mMTC)
Mobile Broadband
Powers high-speed mobile internet with consistent quality of service for streaming, gaming, and cloud applications.
• 4K/8K video streaming
• Cloud gaming services
• Augmented/Virtual reality
IoT Networks
Enables massive IoT connectivity with efficient spectrum usage for smart sensors and industrial monitoring.
• Smart city infrastructure
• Industrial IoT (IIoT)
• Environmental monitoring
Autonomous Vehicles
Critical for V2X communications requiring ultra-reliable, low-latency data exchange for safety-critical decisions in self-driving cars.
Real-Time Services
Supports video conferencing, live streaming, and online gaming with minimal buffering and consistent quality under varying channel conditions.

## Slide 20
15
Advantages & Limitations
Advantages of HARQ
Improved Reliability
Significantly reduces packet errors through intelligent retransmission and combining techniques, achieving 99.999% reliability targets.
Reduced Packet Loss
Combining multiple transmissions maximizes the probability of successful decoding, minimizing data loss in poor channel conditions.
Adaptive Error Control
Automatically adapts to channel conditions—fewer retransmissions in good channels, more robust combining in poor channels.
Spectrum Efficiency
Optimal use of available bandwidth through intelligent redundancy management, especially with IR schemes.
Limitations of HARQ
Increased Latency
Retransmissions introduce delays that can violate ultra-low latency requirements for time-critical applications.
Implementation Complexity
Advanced schemes (especially IR) require sophisticated encoding/decoding algorithms and rate-compatible code design.
Memory Requirements
CC and IR schemes need substantial buffer storage at the receiver to store soft decisions and multiple transmissions.
Power Consumption
Additional processing for combining and advanced decoding increases energy consumption in mobile devices.

## Slide 21
16
Future Research Directions
The evolution of HARQ technology continues with emerging research areas that promise to further enhance wireless communication performance.
AI-Based HARQ Optimization
Leveraging machine learning algorithms to optimize retransmission strategies based on real-time channel conditions and traffic patterns.
• Predictive retransmission scheduling
• Dynamic code rate adaptation
• Intelligent combining strategies
Adaptive HARQ Schemes
Developing context-aware HARQ that dynamically switches between Type I, CC, and IR based on application requirements and channel state.
• Service-specific optimization
• Cross-layer design approaches
• QoS-aware retransmission control
Integration with 6G
Designing next-generation HARQ for 6G requirements including terahertz communications and intelligent reflecting surfaces.
• THz band communication support
• Massive MIMO integration
• Semantic communication paradigms
ML for Channel Prediction
Using deep learning models to predict channel conditions and proactively adjust HARQ parameters before degradation occurs.
• LSTM-based channel forecasting
• Reinforcement learning for HARQ
• Real-time parameter optimization
Research Impact
These research directions aim to achieve near-zero latency and 99.99999% reliability for next-generation wireless applications.

## Slide 22
17
Conclusion
Key Findings
This study comprehensively evaluated three HARQ schemes for 5G NR, demonstrating that HARQ is essential for achieving 5G reliability targets in fading channel environments.
1
Type I HARQ
✓ Simple
✗ Inefficient
Best for resource-constrained devices requiring minimal complexity.
2
Chase Combining
✓ Balanced
✓ Moderate complexity
Ideal for general-purpose applications requiring good performance.
3
Incremental Redundancy
✓ Best performance
✗ Higher complexity
Optimal for 5G high-data-rate and mission-critical applications.
Fundamental Trade-off
The choice of HARQ scheme involves a fundamental trade-off between complexity and efficiency. Application requirements, channel conditions, and device capabilities must be carefully considered to select the optimal approach.
Best Overall Performance
Incremental Redundancy delivers the best BER and throughput performance, making it the preferred choice for 5G NR deployment.
Path Forward
Future research should focus on AI-driven adaptive HARQ and integration with emerging 6G technologies.
Thank You for Your Attention

## Slide 23
I8
References
1 ) Throughput and Delay Analysis of HARQ with Code Combining over Double Rayleigh Fading Channels -
https://drive.google.com/file/d/1N-OrEkbxuYs4QRwbdTpeMklnE2wDYdli/view?usp=sharing
2) Resource Allocation and HARQ Optimization for URLLC Traffic in 5G Wireless Networks
https://drive.google.com/file/d/1PMNAJSdlmasz_vWRyERSJZXWKQkN21Ks/view?usp=sharing
3) Optimized Asymmetric Feedback Detection for Rate-adaptive HARQ with Unreliable Feedback
https://drive.google.com/file/d/1Qx2NJsd29xjYSvTMBcHu1JMaYZAcl1BZ/view?usp=sharing
4) URLLC for 5G and Beyond: Requirements, Enabling Incumbent Technologies and Network Intelligence
https://drive.google.com/file/d/18ZLKuHUWLrPDFYnw_WdtTpKi9yQad_Qj/view?usp=sharing
5) Performance Evaluation of 5G New Radio LDPC over Different Scenarios of Lognormal Fading Channel
https://drive.google.com/file/d/1YbbMUDmyaAqTGB-pGvnqG1AITd0fjF1F/view?usp=sharing